68HC11 Assembler Documentation
                      Version 1.0  11/23/92


Copyright (c) 1992, Brian Mathewson.  All rights reserved.

This is a Forth-based assembler for the Motorola MC68HC11 family
of microprocessors.  It was designed to run on a version of
Forth running on a 68HC11 microprocessor, namely Max-Forth from
New Micros, Inc.  It allows you to easily create code words which
can be called either from other code words, by colon
definitions, or as interrupt routines.

Some features of this assembler are:
  * Support for all 68HC11 opcodes.
  * Small size.
  * Supports all addressing modes.
  * Senses direct addresses (0-FF) and compiles accordingly.
  * Simple, standard op-code format.
  * Supports assembly-based IF, ELSE, THEN, BEGIN, UNTIL, etc.
  * Supports use of the bit test branches with IF, WHILE, UNTIL,
  * Branch offset range checking.

This assembler was designed and written by James Norris
and Brian Mathewson.

Comments and suggestions are welcome.  Please also report any
problems or errors in this program.  Let us know if you have
found this code valuable and how you are using it.

    Brian Mathewson                 James P. Norris
    21576 Kenwood Avenue            1909 Lakeview Avenue
    Rocky River, OH 44116-1232      Rocky River, OH 44116

Internet
    bbm@cleveland.freenet.edu       bo511@cleveland.freenet.edu


                68HC11 Assembler License Agreement

This program or any portion thereof may not be sold or incorporated
into a product in any form without the written consent of the
authors.  However it may be freely distributed in its complete,
un-altered form.

There is no charge for using this program for private, non-
commercial use.  If any portion of this code is used or adapted
to be used in a commercial, military, or otherwise for-profit
environment, a license fee of $15 (US) is required, payable to:

    Brian Mathewson
    21576 Kenwood Avenue
    Rocky River, OH  44116-1232

While an effort has been made to make this program error-free,
this program is presented without guarantees of any kind.  No
responsibility will be taken for any losses or damages due to
use of this program.


                       About Max-Forth

New Micros, Inc. makes a line of single-board computers and
peripherals for them.  They sell an MC68HC11 with their Max-Forth
installed in internal ROM, either as a separate chip or in one
of their boards.  Contact them for more information at:

    New Micros, Inc.
    1601 Chalk Hill Road
    Dallas, Texas 75212
    Tel: (214) 339-2204

Note:  The authors have no affiliation with New Micros other than
       being contented users of their products.


                      Using the Assembler

You will need to use a terminal program to download the assembler
and your source files to the 68HC11 board.  I use a Forth word
called TERMINT on my DOS-based Forth which acts as a dumb terminal
emulator to work in Max-Forth.  I can easily break out of it,
edit my source files, then use a word called CRAM which crams the
source file screens into Max-Forth as if I were madly typing it
all in.  -bbm


                        -=< EXAMPLES >=-

I. General

Code words are defined as follows:

   CODE-SUB <code-word-name>  <instructions>  END-CODE

For CODE-SUB words you will always need an RTS before the END-CODE

   CODE-SUB <code-word-name>  <instructions>  RTS END-CODE

For interrupt routines, use an RTI

   CODE-SUB <irq-code-word>   <instructions>  RTI END-CODE

An example of a typical Forth word is below.  Note that the Y 
register is used as the stack pointer in Max-Forth.

   CODE-SUB DUP   0 ,Y LDD   DEY DEY  0 ,Y STD  RTS END-CODE


The opcode format for using each of the 68HC11's addressing modes is
as follows:

   Examples             Description                Addressing Mode
   --------  ------------------------------------- ---------------
   23 # LDD  loads D with number 23;                  immediate
     28 LDD  loads D with contents of address 28;     direct
    CTR LDD  loads D with contents of VARIABLE CTR;   extended
   4 ,X LDD  loads D with contents of address X+4;    indexed
   0 ,Y LDD  loads D with contents of address Y+0;    indexed

For indexed addressing, the offset can be from 0 to FFh, positive
offsets only.

The compiler will detect extended address that are between 0 and FFh
and compile the instructions with the faster direct addressing mode.


Notice that some of the instructions are named differently from the way
they are typically spelled.  This makes the words more consistent
and more compact.  For example, dropping the extra A in instructions
like LDAB and LDAA, cuts them to just LDA or LDB.  You could also change
CPX, CPY and CPS to CMPX, CMPY, and CMPS to make them more consistent
with CMPA and CMPB, for example.

You can create macros which combine several instructions.  (A few
are included.)  For example, defining the macro below:

    : PSHD  DEY    DEY  0 ,Y STD ;       ( both do the same thing, but )
or  : PSHD  1809 , 1809 , 18ED , 0 C, ;  (  the second form is faster. )

turns
       CODE-SUB DUP   0 ,Y LDD   DEY DEY  0 ,Y STD  RTS END-CODE
into
       CODE-SUB DUP   0 ,Y LDD   PSHD  RTS END-CODE


Here are some more examples.

   CODE-SUB 0!   CLRA CLRB  0 ,Y LDX  0 ,X STD  INY INY  RTS END-CODE

      where  0!  does  : 0! ( addr -- ) 0 SWAP ! ;

   CODE-SUB 1+!  0 ,Y LDX INY INY  0 ,X LDD  1 # ADDD
                 0 ,X STD  RTS END-CODE


II. Conditionals, Branches, Loops

The assembler supports use of structured programming constructs such
as IF, ELSE, THEN, BEGIN, WHILE, UNTIL, REPEAT, with meaningful
conditionals like in Forth.

First, you can create  condition IF, ... ELSE, ... THEN,  structures
like the following:

   CODE-SUB LF?   0 ,Y LDD  10 # CPD      0= IF,  -1 # LDD
                                           ELSE,   0 # LDD  THEN,
                  0 ,Y STD  RTS END-CODE

The following conditions can be used before IF, WHILE, and UNTIL,

   0=  >  <  U>  U<  PLUS

Use NOT after any of the conditionals above results in the opposite
condition.  So,  > NOT  is the same as  <=.  The following are also
equivalent:

     0= NOT   not=0
      > NOT   <=
      < NOT   >=
     U> NOT   U<=
     U< NOT   U>=
   PLUS NOT   MINUS (i.e. negative)
 
NOT just toggles bit 0 of the number on the stack.  If you examine the
opcodes for the branch instructions, you will notice that toggling this
bit will give you the opposite branch.

   CODE-SUB ~LF?  0 ,Y LDD  10 # CPD  0= NOT IF,  -1 # LDD
                                           ELSE,   0 # LDD  THEN,
                  0 ,Y STD  RTS END-CODE


You may also use BSET? and BCLR? before an IF,  These check if bits
are set or clear at a memory location and branch accordingly, such 
as in ODD?, which returns a 1 if bit 0 at address addr is set:

   CODE-SUB ODD? ( addr -- f ) 0 ,Y LDX  1 0 ,X BSET? IF,  1 # LDD
                 ELSE,  CLRA CLRB  THEN,  0 ,Y STD  RTS END-CODE

The formats for BCLR? and BSET? are:

           mask      addr BCLR? IF,                direct addressing
           mask offset ,X BCLR? IF,                indexed addressing
           mask offset ,Y BCLR? IF,                indexed addressing


WHILE, and UNTIL, also take conditions such as  0=, >, or BCLR?  just
as the IF, statement does.  Here are two examples of an ERASE command.

   CODE-SUB ERASE ( addr len -- ) 0 ,Y LDD  2 ,Y LDX
                  BEGIN,  0 ,X CLR  INX  1 # SUBD  0= UNTIL,
                  DROP, DROP,  RTS END-CODE

   CODE-SUB ERASE ( addr len -- ) 0 ,Y LDD  2 ,Y LDX
                  BEGIN,   1 # SUBD  0= NOT WHILE,  0 ,X CLR  INX
                  REPEAT,  DROP, DROP,  RTS END-CODE

Both accomplish essentially the same thing, although the second will
clear one less byte (the last) than the first one.  However, given a
length of 0 both will try to clear all of memory.  To limit them to
clearing 32767 bytes (a reasonable limit for a 64K address space), add
an IF, ... THEN, as follows:

   CODE-SUB ERASE ( addr len -- ) 0 ,Y LDD  2 ,Y LDX
                  0 # CPD > IF,
                    BEGIN,   1 # SUBD  0= NOT WHILE,  0 ,X CLR  INX
                    REPEAT,
                  THEN,  DROP, DROP,  RTS END-CODE


You can use BCLR? and BSET? with UNTIL, and WHILE, also:

BEGIN, ... mask      addr BCLR? UNTIL,             loop until bit clear
BEGIN, ... mask offset ,X BSET? WHILE, .. REPEAT,  loop while bit set


One last example is a neat algorithm for finding an integer SQRT:

   VARIABLE CNT
   CODE-SUB SQRT  1 # LDX  CNT STX  0 ,Y LDD
                  BEGIN,  CNT SUBD  PLUS WHILE,  INX INX  CNT STX
                  REPEAT, XGDX  LSRD 0 ,Y STD  RTS END-CODE


For creating code words which do not have straight IF, .. ELSE, .. THEN,
structures, you can combine multiple IF,'s ELSE,'s and THEN,'s and use
use SWAP or OVER or something to get it right.

For example, if you have a word that should jump around like this:

                                                  __________3_________
                          _____________1_________/___                 \
                         /                      /    \                 \
CODE-SUB FROG  part1  IF,-->part2 IF,-->part3->/  ELSE,-->part4  part5  THEN,
                                     \_____________2____________/

you can code it like this:
                                        Branches on stack
CODE-SUB FROG   part1  condition IF,         ( 1 )
                part2  condition IF,         ( 1 2 )
                part3     SWAP ELSE,         ( 2 3 )
                part4     SWAP THEN,         ( 3 )
                part5          THEN,
         RTS END-CODE

Notice that IF, puts a branch on the stack, THEN, resolves a branch,
and ELSE, resolves one branch but adds a new one.


Two more useful words are JSR' and BSR.  JSR' <code-word> will execute
any <code-word> that was defined with an RTS before END-CODE.  So, you
can do this:

   CODE-SUB HOP     0 ,Y LDX   10 # LDA  0 ,X STA  INY INY RTS END-CODE

   CODE-SUB RIBBIT  JSR' FROG   ' HOP CFA 2+ BSR  RTS END-CODE

The word RIBBIT compiles a long JSR to frog, then compiles a short JSR
to HOP.  If you want, define a BSR' just like JSR'

The JMP and JSR instructions are also defined.  JSR' is just a shortcut
for writing  ' <code-word> CFA 2+ JSR  (i.e. JSR to extended address.)

The BSR instruction is limited to just a relative jump, while you can
use direct, extended and indexed addressing modes with JSR and JMP.
The only reason to use BSR is for smaller code size or for relocatable
code (they take the same number of cycles to execute.)



III.  Bit Instructions

The bit instructions BCLR and BSET either set or clear bits at a memory
location.  Their form is:

     mask  dir_addr  BCLR   direct addressing  (dir_addr=direct address)
     mask  offset ,X BCLR   indexed addressing
     mask  offset ,Y BCLR   indexed addressing

BSET works the same way.

Some examples are:

     40    28 BCLR   clears bit 6 (of 0-7) of memory location 28.
      3  8 ,X BSET   sets bits 0 and 1 at memory location X+8.


The opcodes BRCLR and BRSET are implemented as BCLR? and BSET?

For BCLR? and BSET? (branch on bit clear or bit set) the opcodes are
defined in reverse so that they work logically with IF, WHILE, and
UNTIL, words.

           mask      addr BCLR? IF,                direct addressing
           mask offset ,X BCLR? IF,                indexed addressing
           mask offset ,Y BCLR? IF,                indexed addressing

Again, BSET? works the same way.  Use them with UNTIL, and WHILE, also:

BEGIN, ... mask      addr BCLR? UNTIL,             loop until bit clear
BEGIN, ... mask offset ,X BSET? WHILE, .. REPEAT,  loop while bit set

Some examples are:

ODD sets bit 0 of the byte at addr to a 1.

   CODE-SUB ODD ( addr -- ) 0 ,Y LDX  INY INY  1 0 ,X BSET
            RTS END-CODE


SCAN scans from addr1 until it finds a byte with the MSB bit 7 set
and returns with the address of that byte.

   CODE-SUB SCAN ( addr1 -- addr2 )  0 ,Y LDX
                 BEGIN,  80 0 ,X BCLR? WHILE,  INX REPEAT,
                 0 ,Y STX  RTS END-CODE


IV.  Design Notes

This assembler will not correctly compile extended addresses which
refer to locations FFFD-FFFF (-3 to -1) as these are reserved for the
addressing mode switches #, ,X and ,Y.

IF, adds 20h to the number on the stack and compiles it into memory
and then compiles the branch offset.  For condition codes the number
on the stack +20h becomes the branch opcode.  For the BCLR? and BSET?
IF, instead compiles the mask byte and then the branch offset.  The
BCLR? and BSET? compile the opcode and address/offset of the BRSET 
and BRCLR instructions.

For conditionals IF, statements take a number, 0-15 which specifies
which branch instruction gets compiled at the IF,.  Notice that you
should specify the OPPOSITE branch for each condition.  If you want
to do a 0= IF, then 0= must be defined as a 6 CONSTANT 0= for the 
opcode 26h = BNE (branch on not=Zero)  Then, if the condition is =0,
it will not branch and will execute the instructions after the IF,

So, if you want a specific branch at the IF, then just put the number
of the branch opcode minus 20h in front of the IF,  To compile the
equivalent of specific branch instructions such as BMI, use the
following conditionals before IF, WHILE, or UNTIL,

   5 CONSTANT CC   4 CONSTANT CS   6 CONSTANT EQ  D CONSTANT GE
   F CONSTANT GT   3 CONSTANT HI   5 CONSTANT HS  E CONSTANT LE
   4 CONSTANT LO   2 CONSTANT LS   C CONSTANT LT  A CONSTANT MI
   7 CONSTANT NE   B CONSTANT PL   9 CONSTANT VC  8 CONSTANT VS
   1 CONSTANT ALWAYS               0 CONSTANT NEVER

Then, to have the equivalent of BMI, use  MI IF,  which actually
compiles a BPL (the opposite of BMI).

This assembler will not catch errors such as 5 # STX but will catch an
error in 5 # CLR and similar instructions.  This is because an easy way
to check if immediate or direct addressing is allowed is to see if the
opcode is <80h.

Although automatic direct mode addressing is used, the compiler
correctly senses when direct addressing is not available and uses
extended addressing instead, such as in 28 CLR.

The following instructions are named differently than in the Motorola
literature (in order to make them simpler and more consistent):

 LDA = LDAA, LDB = LDAB, ORA = ORAA, ORB = ORAB, STA = STAB, STB = STAB.

You could also change CPX, CPY and CPS to CMPX, CMPY, and CMPS to make
them more consistent with CMPA and CMPB, for example, or vice versa.

The only instruction not included is 00 INH TEST because it may only be
used in test modes, which is rarely needed.

If this assembler is used with any other Forth than Max-Forth, it must:
  - have TRUE=FFFF ( and not =1 ) after > (see CPLEXT).
  - give an error if the stack changed between CODE-SUB and END-CODE
    (or the equivalents to CODE-SUB and END-CODE.)

Although it is obvious, remove anything you do not use (including
comments) to reduce the size of the assembler and the loading time.
You can also eliminate much of the error checking and error messages
if you are comfortable with this (or keep two versions around.)
Or, save the assembler into EPROM for fast startup times.


Enjoy.

Copyright (c) 1992, Brian Mathewson.  All rights reserved.
End of 68HC11 Assembler Version 1.0 Documentation  BBM JPN 11/23/92